## Slide 1: Clinical Psychophysiology
September 11 & 16, 2008
Notes: BNC history:P
U. of Florida, 1981-1998
2 NIMH, 1998 - 2005 (Chief, Adult Psychopathology & Prevention Research Branch
3 Applied interests in emotions and disorders

## Slide 2: Basic electronics in psychophysiology
Need to understand how electronics affects the measurements that we use
Conceptual and practical aspects of making recordings
Safety
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard:

## Slide 4
*

## Slide 5
1/1,000 = 1 * 10-3
= 1 milliamp, millivolt
(mamp, mv)
1/1,000,000 = 1 * 10-6
= 1 microamp, 1 microvolt
(µa, µv)
Units of Measure
A simple example:
Volts across 3000 ohm resistor: 9 V
(in opposite direction from battery)
-- “Conventional” current flow vs. electron flow
+

## Slide 6
3000 Ω
6000 Ω
What is the total resistance?
6K + 3K = 9K
A more complicated example

## Slide 7
3000 Ω
6000 Ω
What is the total resistance?
6K + 3K = 9K
What is the current?

## Slide 8
3000 Ω
6000 Ω
What is the total resistance?
6K + 3K = 9K
What is the current?
I=E/R
I=9/9000
I= 0.001 amp
= 1 mamp

## Slide 9
3000 Ω
6000 Ω
Voltage across the 6K resistor?
E = IR
= .001 * 6000
= 6 V

## Slide 10
6000 Ω
3000 Ω
What is the total resistance?
6K + 3K = 9K

## Slide 11
6000 Ω
3000 Ω
What is the total resistance?
6K + 3K = 9K
What is the current?
I = 9/9000 = .001 amp
= 1 mamp

## Slide 12
6000 Ω
3000 Ω
Voltage across the 3K resistor?

## Slide 13
6000 Ω
3000 Ω
Voltage across the 3K resistor?
E = IR
= .001 * 3000
= 3 V

## Slide 14
Parallel Resistors
R3
R2
R1
R1.2 = R1 * R2
R1 + R2
R1 = 4000, R2 = 12,000
= 4000 * 12,000
16,000
R 1.2 = 3,000 ohms *(3K)
I.e., less than either R singly (water analogy: multiple channels)

## Slide 15
Parallel Resistors: Continued
R3
R2
R1
R 1.2 = 3,000 ohms
R3 = 6,000 ohms
V (R3) = ?
V (R1.2) = ?
I = ?

## Slide 16
Parallel Resistors: Continued
R3
R2
R1
R 1.2 = 3,000 ohms
R3 = 6,000 ohms
V (R3) = ?
V (R1.2) = ?
I = 9 / (6K + 3K) = 9/9K = .001 = 1 mamp

## Slide 17
Parallel Resistors: Continued
R3
R2
R1
R 1.2 = 3,000 ohms
R3 = 6,000 ohms
V (R3) = .001 * 6K
= 6 V
V (R1.2) = .001 * 3K
= 3K
I = 9 / (6K + 9K) = 9/9K = .001 = 1 mamp

## Slide 18
Parallel Resistors: Continued
R3
R2
12,000
R1
4,000
R 1.2 = 3,000 ohms
R3 = 6,000 ohms
I (R1) = E/R
= 3/4,000
= 0.75 mamp
I = 9 / (6K + 9K) = 9/9K = .001 = 1 mamp
3V “dropped”
I (R2) = E/R
= 3/12,000
= 0.25 mamp
6V “dropped”
Total I, R1 & R2: 0.75 + 0.25 = 1 mamp

## Slide 19
6000 Ω
1,000,000 Ω
Some implications of Ohm’s law:
The larger the resistance,
the more voltage is dropped
across it. Therefore, keep
electrode resistances low
Want a very high resistance
in the bioamplifier; this
minimizes current flow in the
circuit, avoids “loading” the
low-current source
Low resistances also help
avoid antenna effects along
the electrode cables.

## Slide 21
6000 Ω
1,000,000 Ω
Differential vs. single-ended
Inputs to amplifier

## Slide 22
Differential vs. single-ended

## Slide 23
Standard amplifiers: single-ended Input & output
Bioamplifiers: Differential input single-ended output

## Slide 24
Voltage:
Ground:

## Slide 25
Time domain

## Slide 26
Frequency domain
Decibel = dB =
20 * log (V1/V2)
Cutoff frequency =
“3 dB down”, I.e.:
20 * log (.707/1) =
20 * -.15 = -3.01

## Slide 27
Frequency domain
Time constant = 200 ms
fc?

## Slide 28
Frequency domain
Time constant = 200 ms
fc?
fc = 1/(2*3.14*0.2)
fc = 0.8 Hz

## Slide 29
Frequency domain
Want fc of 2 Hz.
TC setting?

## Slide 30
Frequency domain
Want fc of 2 Hz.
TC setting?
TC = 1/(2*3.1416* fc)
TC = 0.079 s, 79 ms

## Slide 31
Frequency domain
“skirt”
Want TC of 5 sec.
fc setting?
fc = 1/(2*3.1416* 5)
fc = 0.031 Hz

## Slide 32
Summary:
Time constant Cutoff frequency
79 ms 2 Hz
200 ms 0.8 Hz
5000 ms 0.031 Hz
Thus, the LONGER the time constant, the
LOWER the cutoff frequency

## Slide 33
Octave: = doubling of frequency

## Slide 34
Grass Instruments: time constant chart

## Slide 40
E.g., important for zero-crossing scoring algorithms

## Slide 41
True Integration: Constantly integrate input signal

## Slide 43
“Averagor” integrator: Actually, a capacitor signal

## Slide 44
“Averagor” integrator: Actually, a capacitor signal
Would like an envelope representation of input signal;
How to get it?

## Slide 45
Rectification: absolute value of signal input
(analog or digital); NB, output frequency is doubled

## Slide 46
“Averagor” integrator: capacitor-coupled
Time constant can be adjusted to fit signal
Long time constant
Short time constant

## Slide 47: Two major types of filters
1) Finite impulse response (FIR): Given a string of 0’s with a single “1” (impulse), output will return to 0 eventually (no feedback)
2) Infinite impulse response (IIR): Given an impulse, the output will (theoretically) never return to 0, due to feedback
Can be analog or digital; an RC circuit is the simplest IIR filter, as the output is exponential
Well-known analog IIR filters: Butterworth, Bessel, Chebyshev
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard:

## Slide 48: Two major types of filters
IIR filters are more common in analog circuits because they are based on RC circuit designs
Digital filters are increasingly popular with greater computer power
Typically, the “raw” signal is saved so one can try different filter algorithms
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard:

## Slide 49: IIR filter considerations
IIR: can design more efficient filters with shorter algorithms
IIR: easier to get sharper cutoff frequency definition
IIR: But, IIR has non-linear phase distortion across frequencies; may or may not be a problem
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard:

## Slide 50: FIR filter considerations
FIR: typically involve longer, more complex algorithms
FIR: More difficult to get sharper cutoff frequencies, steep “skirts”
FIR: FIR has linear phase distortion across frequencies,so phase is maintained
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard:

## Slide 51
Digital filtering: Increasingly popular
Simplest FIR: moving average filter (e.g., 4 points)
0 0 0 0 0 10 30 10 0 0 0 0 0
0 0 2.5 10 12.5 12.5 10 2.5 0 0

## Slide 52
Digital filtering: Increasingly popular
Simplest: moving average filter (e.g., 4 points)
0 0 0 0 0 10 30 10 0 0 0 0 0
0 0 2.5 10 12.5 12.5 10 2.5 0 0

## Slide 53
Digital filtering: Increasingly popular
Simplest: moving average filter (e.g., 4 points)
0 0 0 0 0 10 30 10 0 0 0 0 0
0 0 2.5 10 12.5 12.5 10 2.5 0 0

## Slide 54
Digital filtering: Increasingly popular
Simplest: moving average filter (e.g., 4 points)
0 0 0 0 0 10 30 10 0 0 0 0 0
0 0 2.5 10 12.5 12.5 10 2.5 0 0

## Slide 55
Digital filtering: Increasingly popular
Simplest: moving average filter (e.g., 4 points)
0 0 0 0 0 10 30 10 0 0 0 0 0
0 0 2.5 10 12.5 12.5 10 2.5 0 0

## Slide 56: Computer arithmetic
Binary: powers of 2 (sets of on/off switches)
Binary Digit = bit
Byte = 8 bits
Binary numbering:
0 = 0
1 = 1 decimal
10 = 2 decimal
11 = 3 decimal
01111111 = 1+2+4+8+16+32+64 = 127
11111111 = 1+2+4+8+16+32+64+128 = 255
2 bytes = 16-bit word, 32767 to -32768, or 0 to 65535
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard:

## Slide 57: 4 ways that bits are used in computers
Program code (assembler, compiler, linker)
Numeric data
ASCII data (codes) [American Standard Code for Information Interchange)
Patterns of bits used to read or control the environment
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard:

## Slide 59
20 ------- 1 volt -------- 2047
10 ------- 0 volt --------- 0 A/D
0 ------- -1 volt ------- -2048
µs

## Slide 60
**

## Slide 62: Parallel vs. serial ports
Digital inputs/outputs: TTL (transistor-transistor logic)
The 2 values are 0 V or +5 V
Digital I/O often uses parallel ports (older printer standard)
Serial port data: RS-232 or RS-422
Typically sends ASCII data (codes)
+3-15 V = “Off”; – 3-15 V = “on” (0 V = undefined)
Notes: “any strong feeling” -- Princeton
“ … emotion is the language of a person’s mental state of being, normally based in or tied to the person’s internal (physical) and external (social) sensory feeling. Wikipedia.
Izard: emotion experience is “a feeling state or motivational condition, a direct and immediate product of the particular neural processes associated with that emotion”
Izard: 9 emotions: interest, enjoyment, surprise, distress, disgust, anger, shame, fear, contempt.”
Any of them: sex, jealousy?
“OUP: “incidents of coordinated changes in several areas, including what has been called the “reaction triad” of physiological arousal, motor expression, and subjective feeling, in response to either an internal or an external event of significant importance to an individual”
“feelings such as happiness, sadness, anger, elation, irritation, etc. The specific definition of emotion is difficult to qualify as it is a completely subjective experience.” access.autistics.org
Panksepp: presents six basic emotion systems
Ekman: specific emotions are: happiness, interest, surprise, feaer, anger, sorrow, disgust.
Izard: